1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - JDAM, LJDAM, WCMD

Master Arm ... ON
Master Mode ... A/G

TGP switch ... ON (left instrument panel), takes 60 seconds to warm up
LASER switch ... ARM (left instrument panel)

JDAM, LJDAM, and WCMD with TPOD
LJDAM: Set laser code on bomb TODO
  - LJDAMs are just like JDAMs, but if you're lasing, they will follow the laser dot.
1. Set up bombs as you would for CCRP.
2. Designate target with TGP and set SPI to target location (Gray Reset Hat forward long).
3. Circular reticle on HUD shows range: Triangle carets are the Max and Min range. When you start getting close, the inner circle starts "unwinding" counterclockwise showing the current range. When current range line is between the carets, you're in range, and MAN REL is displayed on the left side of HUD.
4. When in range, press AND HOLD Red Button until the bomb drops.
  - If you don't hold the button down until the bomb drops, you'll get a red "IAM LAUNCH ABORTED" warning. Press TMS left (Gray Reset Hat left) to clear (clears all WCN warnings). See steps below to reset.

Reset hung store (IAM LAUNCH ABORTED) -- WIP needs verification
1. Recommended to be in level flight and put on autopilot because this is going to take a minute...
2. Remember which station is "hung", and type of weapon.
3. Go to DSMS -> INV page.
4. Select hung station.
5. Select weapon type (bomb, cbu, gbu, missile, pod).
6. Select weapon by name.
7. Click load station / symmetrical.
8. Click on STAT OSB to return to main DSMS page.
9. On main DSMS page, select station belonging to hung store (smart station are marked "1760")
10. Select power on station belonging to hung store to clear failed status.
11. After that find LOAD page on one of the MFDs (if not shown across the bottom, you must press and hold one of the bottom OSBs to show).
12. Select LOAD DSMS OSB.
13. When load is complete, go to DSMS page and store should be usable again.