1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

601 - Notes, Quirks, and Trivia

On MFDs, fields with "[]" can be changed by entering a new value in the UFC scratchpad first, then press the OSB next to the field. Fields with "↕" will cycle through several values when the OSB is pressed multiple times.

General flow for non-gun weapons:
1. Select weapons on DSMS page or by setting SOI to HUD and pressing DMS left/right (Middle Finger Hat left/right).
2. Select CCIP/CCRP mode by pressing Lower Gray Button to cycle HUD mode.
3. Fire with Red Button.

General flow for designating targets:
1. Set SOI to whatever you want to designate with.
2. Press China Hat back short (Rear Thumb Button short) to re-center the sensor on the nose or boresight.
3. Point the sensor at the target.
4. China Hat forward short (Front Thumb Button short) generally toggles FOV.
5. Press TMS forward short (Gray Reset Hat forward short) to lock, and/or TMS forward long (Gray Reset Hat forward long) to set target as SPI.
6. Press China Hat forward long (Front Thumb Button long) to point all sensors at the SPI.
7. SPI cannot be undesignated, only redesignated to a new location.

Differences between A-10C and A-10C II, as of 02/12/2024:
- Weapon differences: C II carries LJDAM, APKWS, AGM-65L
- HOTAS differences
  - Broadcast SPI: C = DMS right long; C II = TMS right long
  - Boresight TGP: C = China Hat aft; C II = no HOTAS command, press T5 OSB on TGP page or set to STBY then A/G
  - Set last SPI as markpoint: C = can't do it, have to hook markpoint and set as SPI; C II = TMS right long
  - TMS down on C is swap MFDs, on C II is SOI to HMD.
  - TMS up long on C II is message quick look, no func on C
  - C II has HMD controls on HOTAS