1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

204 - Ground - Shutdown

Shutdown -- WIP, steps from manual, needs verification
1. Parking brake ... Set (hold parking brake button, hold toe brakes, release parking brake button, release toe brakes)
2. Heater function switch ... OFF (roof console forward left)
3. AFCS SYSTEM SEL knob ... OFF (center angled console middle)
4. MFDs ... OFF
5. APU switch ... RUN for 5 seconds, START for 2 seconds, then back to RUN
6. When APU RDY light is on, continue.
7. APU GEN switch ... ON
8. GEN 1 and GEN 2 switches ... OFF (wait 2 seconds in between)
9. ENG COND levers ... GROUND
10. XFEED switch ... CLOSE
11. All FUEL PUMP switches ... OFF
12. ENG COND levers ... STOP (technically you should wait 2 minutes after switching to GROUND to allow cooldown)
13. B/U PWR switch ... OFF
14. PWR XFER 1 and PWR XFER 2 switches ... OFF
15. APU GEN switch ... OFF
16. APU switch ... OFF
17. BATT switch ... OFF