1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

306 - Flight - DAFCS, LCT, DASH

DAFCS (Digital Advanced Flight Control System)
- WIP: Many of the DAFCS functions are not yet implemented as of 2024-11-1.
- Over 40 kts, will automatically coordinate turns and ground track.

LCT (Longitudinal Cyclic Trim)
- LCT basically automatically tilts the rotors forward/aft to allow the fuselage to stay level at both hover and high speeds.
- LCT controls are on the CYCLIC TRIM and SYSTEM SEL panels (center angled console middle)
- CYCLIC TRIM panel
  - When in AUTO mode, LCT will be set automatically.
  - When in MANUAL mode, the FWD and AFT switches control the trim of the rotors.
  - EXT means the rotors are tilted forward, RET means they're tilted back (relative to default GND (Ground) position).
  - The MFD VSD page shows the current trim position.
- SYSTEM SEL knob:
  - BOTH means both flight control computers are active.
  - 1 or 2 means only that single flight control computer is active.
  - OFF means neither flight control computer is active. CYCLIC TRIM panel switches are still active though.
- For pinnacle landings, recommended to set LCT to MANUAL and set the rotors to GND position. Otherwise the weight-on-wheel switches in the aft gear may trigger unexpectedly and cause the trim to change.

DASH (Differential Airspeed Hold)
Over 40 kts, automatically feeds in forward cyclic trim so you don't have to hold the stick all the way forward at high speed.