1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

403 - A2A - Radar Auto Acquisition modes

Auto Acquisition Modes -- WIP
- Use Auto Acquisition ("Auto Acq") switch (Gray Reset Hat) to select modes.
- Auto Acq modes must start from Search. Press Auto Acq press to undesignate from any mode and return to search.
- Super Search
  - Auto Acq forward short enters Super Search, subsequent presses cycle Boresight/Super Search mode.
  - 20x20 deg search, about the size of the HUD, 500 ft to 10 nmi range. HUD shows large circle.
  - TDC up/down to bias the search up/down, HUD circle moves up or down, but real search area is about one HUD-height above or below.
  - Auto Acq forward short again to go to Boresight mode (see below)
- Boresight
  - Auto Acq forward short enters Super Search, subsequent presses cycle Boresight/Super Search mode.
  - 4 deg circle centered on aircraft waterline, 500 ft to 10 nmi range.
- Long Range Boresight
  - Auto Acq forward long.
  - 2 deg circle on aircraft waterline, 3000 ft to 40 nmi range.
  - NOTE This may allow you to burn-through jamming and lock a target that you couldn't acquire otherwise.
- Vertical Scan
  - Auto Acq aft short.
  - 5 deg above waterline to 55 deg, 500 ft to 10 nmi range.
- Auto Guns aka Guns
  - Selected when you select guns with weapon select switch aft (Pinky Switch up)
  - 15 nmi range for locking, but shows targets out to 20 nmi on radar screen
  - TDC moves search zone as if looking through boresight (e.g. az/el view)
  - Coolie hat up (Middle Finger Hat up) while in guns mode toggles funnel/line gunsight