1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A2G - Radar HRM

General flow for HRM -- Front Seat
1. Go to A/G radar page, take command, and set to RBM mode initially (B1 OSB).
2. Set the cursor function to MAP (B2 OSB).
3. Find target area. Jump cursor directly to a Sequence Point by entering SP number on scratchpad and pressing T4 OSB.
4. Use Gray Reset Hat forward/aft to change the HRM map size.
5. FREEZE mode -- At any time, either in RBM mode or with a HRM map, press Pinky Button to toggle FREEZE. The current scan or map will finish, and then radar will deactivate. Press TDC press again to do a new map, or toggle freeze mode off to resume continuous mapping.
6. Press TDC press to begin mapping.
7. HRM page settings:
  1. Press L3 OSB to toggle ML1/ML2. ML2 gives better map quality, takes 1.5x longer.
  2. Press L2 OSB to toggle STB/progressive?? STB (stabilized) means continuous re-maps will be on the same ground location, progressive means new map location will move with the plane.
  3. Press R2 OSB to go to HRM PPI mode, which clears the current map and returns to a large-scale HRM similar to RBM. Note grazing angles make it not very useful at low altitude.
  4. Press R1 OSB to store the current map (only possible when in FREEZE mode). Press B5 OSB to toggle NEW/OLD, to show current and previous map image. New maps will always overwrite the map currently being displayed and the current map will become the OLD map.
8. When you have a map of the target, change cursor mode to TGT (B2 OSB). Press TDC press to designate a target on the map.
  - In HRM, recommended to designate small targets (e.g. vehicles) on bottom edge of radar return. Due to radar physics, this will correspond more closely with the actual center of the target.

General flow for HRM -- Back Seat -- TODO
1. With A/G radar on left MFDs, all controls on Throttle Grip:
  1. Take command of Radar MFD ... Middle Finger Hat left/right
    - Radar MFD must be In Command to use controls.
  1. Slew cursor ... TDC ministick
  2. Set cursor action ... Top Hat (fwd=MAP, back=TGT, up=CUE, down=UPDT)
  3. "Quick Step" (moves cursor to next steerpoint) ... Top Hat press
  4. Perform cursor action (Map, Designate, Cue, or Update) ... Rear Thumb Button ("Trigger full-action")
  5. Map size increase/decrease ... Bottom Hat forward/back
  6. Undesignate ... Bottom Hat press
  7. Freeze/Unfreeze toggle ... Pinky Button press
  8. Expand (zoom) HRM map ... Hold Forward Thumb Button ("Trigger half-action"), then press TDC Press
2. With A/G radar on right MFDs, all controls on Joystick:
  1. Take command of Radar MFD ... Shift-Dish Hat left/right
    - Radar MFD must be In Command to use controls.
  1. Slew cursor ... Dish Hat
  2. Set cursor action ... Trim Hat (up=MAP, down=TGT, left=CUE, right=UPDT)
  3. "Quick Step" (moves cursor to next steerpoint) ... Trim Hat press
  4. Perform cursor action (Map, Designate, Cue, or Update) ... Trigger Stage 2 ("Trigger full-action")
  5. Map size increase/decrease ... Gray Reset Hat forward/back
  6. Undesignate ... Gray Reset Hat press
  7. Freeze/Unfreeze toggle ... Lower Gray Button press
  8. Expand (zoom) HRM map ... Hold Trigger Stage 1 ("Trigger half-action"), then press Dish Hat Press