1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501a - A2G - Radar HRM ranges and grazing angles

HRM patch map ranges and grazing angles
HRM patch map sizes and ranges
Map size	Max range
80	160 nmi
40	160 nmi
20	160 nmi
10	160 nmi
4.7	80 nmi
3.3	50 nmi
1.3	40 nmi
.67	40 nmi

- Grazing angles:
  - Best grazing angle is 2-10 degrees down from the nose, minimum usable angle is 0.5 degrees down from the nose, max is 20 degrees down.
  - Rule of thumb: For a 1 deg grazing angle, be at 1000 ft altitude per 10 nmi distance.
  - Map accuracy is better toward the edges of the gimbal, +/- 60 deg.
  - Formulas
    - tan(90 - grazingAngle) = range / alt
    - alt = (rangeNmi * 6076.12) / tan(90 - grazingAngle)
    - range = tan(90 - grazingAngle) * alt
- Grazing angle altitude/range table:
Range / (nmi)	Altitude (ft) for grazing angle					Notes
	-0.5°	-1°	-2°	-10°	-20°	Alt is ft above target
5	265	530	1,061	5,357	11,058
10	530	1,061	2,122	10,714	22,115
15	795	1,591	3,183	16,071	33,173
20	1,061	2,121	4,244	21,428	44,231
25	1,326	2,651	5,305	26,785	55,288
30	1,591	3,182	6,365	32,142	66,346
35	1,856	3,712	7,426	37,498	77,403
40	2,121	4,242	8,487	42,855	88,461	max 0.67 HRM range
45	2,386	4,773	9,548	48,212	99,519
50	2,651	5,303	10,609	53,569	110,576	max 3.3 HRM range
55	2,916	5,833	11,670	58,926	121,634
60	3,182	6,364	12,731	64,283	132,692
65	3,447	6,894	13,792	69,640	143,749
70	3,712	7,424	14,853	74,997	154,807
75	3,977	7,954	15,914	80,354	165,865
80	4,242	8,485	16,975	85,711	176,922	max 4.7+ HRM range