1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201a - Ground - Cold Start - Pilot

Cold Start -- Pilot
1. Helmet ... Put on (right canopy rail)
2. Cartridge start:
  1. ENGINE MASTER switches LEFT and RIGHT ... ON (left console middle inboard)
  2. Tell Crew Chief to load cartridges ... Jester UI -> Crew Chief -> Air Source -> Load Start Cartridges
  3. Start right engine:
    1. ENGINE START switch ... R (right-click) and hold for a couple seconds (left console middle inboard)
    2. At 10% RPM, press and hold right ignition (B6 button), then advance throttle to idle detent (B3 button).
    3. When EGT increases (engine ignition), release ignition (B6 button).
    4. At 65% RPM (idle): R GEN (generator) switch ... ON (forward, right-click) (right console middle outboard)
  4. Start left engine:
    1. ENGINE START switch ... L (left-click) and hold for a couple seconds (left console middle inboard)
    2. At 10% RPM, press and hold left ignition (B4 button), then advance throttle to idle detent (B1 button).
    3. When EGT increases (engine ignition), release ignition (B4 button).
    4. At 65% RPM (idle): L GEN (generator) switch ... ON (forward, right-click) (right console middle outboard)
3. Ground cart start:
  1. Jester UI -> Crew Chief -> External Power -> Connect
  2. When connected: L GEN and R GEN switches ... EXTERNAL (aft, left-click) (right console middle outboard)
  3. Start right engine:
    1. Jester UI -> Air Source -> Connect To Right Engine
    2. ENGINE MASTER RIGHT switch ... ON
    3. Jester UI -> Air Source -> Start Airflow
    4. At 10% RPM: Right Ignition button ... Press and hold, advance right throttle to HALF, then back to IDLE detent, release button
    5. At 65% RPM (idle): Jester UI -> Air Source -> Stop Airflow
    6. R GEN switch ... ON (forward) (right console middle outboard)
  4. Start left engine:
    1. Follow steps above for left engine.
  5. R GEN switch ... Cycle to OFF, then ON (forward) (not sure if this is necessary??) (right console middle outboard)
  6. Jester UI -> Air Source -> Disconnect
  7. Jester UI -> External Power -> Disconnect
4. When engines are started, Jester should prompt to start alignment, and alignment type.
  1. Full alignment may take up to 9 mins?? Depends on ambient temperature??, drift 3.0 nmi/hr.
  2. BATH (Best Available True Heading) alignment takes 2m15s, drift approx 5.5 nmi/hr.
  3. HDG Memory Alignment takes 2m15s, drift 3.0 to 5.5 nmi/hr.
5. Radio mode knob ... T/R or T/R+G (right console middle inboard)
6. IFF ... NORM (right console middle inboard)
7. Radar altimeter ... ON and set bug as desired (instrument panel left)
8. When Jester calls "Set primary and sync":
  1. Attitude reference switch ... PRIM (instrument panel next to artificial horizon)
  2. Compass mode knob ... SYNC (left click) and hold for a few seconds (right console far rear inboard)
9. Sight Mode knob ... CAGE (UFC)
10. RWR ... On (POWER button under RWR display, instrument panel right)
  - Jester will turn on the RWR when the alignment is finished.
1. DSCG switch ... RADAR (center console left)
2. Oxygen supply levers ... ON and NORMAL OXYGEN (left console forward inboard)
3. CADC Corrections switch ... RESET CORR for a few seconds, then back to NORM (left console middle inboard)
4. Altimeter ... Turn and hold RESET lever for 3 seconds to clear red STBY flag, then set QNH or QFE (instrument panel middle)
  - Do this only after the CADC Corrections switch??
1. Standby Attitude Indicator ... Uncage and center (instrument panel lower right)
2. ADI Flight Director switch ... Horizontal (On) (flat knob on Navigation Mode Selector knob, instrument panel bottom, under Standby ADI)
3. YAW, ROLL, and PITCH STAB. AUG switches ... ENGAGE (left console rear inboard)
4. Trim ... 1 to 3 units nose down (3 recommended) (trim guage is on left forward angled panel outboard)
5. Anti-skid ... ON (left console forward outboard)