1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201b - Ground - Cold Start - WSO

Cold Start for WSO -- WIP needs verification
1. Alignment, after both generators are running on internal power:
  1. Navigation Computer Mode knob ... STBY (right console rear inboard)
  2. BATH alignment (fast, ~3-4 min):
    1. INS Power knob ... STBY (must be moved briefly to STBY to avoid INS no-go)
    2. INS Power knob ... ALIGN
    3. When Align light illuminates, alignment is complete.
    4. INS Power knob ... NAV
  3. Heading memory alignment (fast, may be more accurate than BATH, only if aircraft was aligned, parked for less than 2 hours, and not moved):
    1. INS Align Mode switch ... HDG MEM (forward) (red guarded switch)
    2. INS Power knob ... STBY (must be moved briefly to STBY to avoid INS no-go)
    3. INS Power knob ... ALIGN
    4. When Align light starts flashing, alignment is complete.
    5. INS Power knob ... NAV
  4. Gyrocompass alignment (full, ~13m20s):
    1. INS Power knob ... STBY
    2. Heat light should come on. Wait for Heat light to go off (approx 5m50s from standard temp (59 deg F), depends on ambient temp, 20 degF per min, needs to get to 160 degF, plus 50 seconds once at 160). When Heat light is off, proceed.
    3. INS Power knob ... ALIGN
    4. When Align light illuminates (~3-4 min), BATH alignment is complete. Wait.
    5. When Align light flashes (~3m45s), full Gyrocompass alignment is complete.
    6. INS Power knob ... NAV
2. More steps TODO...