1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Auto Start - Pilot

Default auto start takes 5m50s.

After Auto Start -- Pilot -- WIP
1. When engines are started, Jester should prompt to start alignment, and alignment type.
  1. Full alignment may take up to 9 mins?? Depends on ambient temperature??, drift 3.0 nmi/hr.
  2. BATH (Best Available True Heading) alignment takes 2m15s, drift approx 5.5 nmi/hr.
  3. HDG Memory Alignment takes 2m15s, drift 3.0 to 5.5 nmi/hr.
2. Master Caution ... Reset (shift-Trim Hat press, or button on right console far forward inboard)
3. Radio mode knob ... T/R or T/R+G (right console middle inboard)
4. IFF ... NORM (right console middle inboard)
5. Radar altimeter ... ON and set bug as desired (instrument panel left)
6. When alignment is done, Jester calls "Set primary and sync":
  1. Compass mode knob ... SYNC (left click) and hold for a few seconds (right console far rear inboard)
7. Sight Mode knob ... CAGE (UFC)
8. RWR ... On (POWER button under RWR display, instrument panel right)
  - Jester will turn on the RWR when the alignment is finished.
1. DSCG switch ... RADAR (center console left)
2. Oxygen supply lever ... NORMAL OXYGEN (left console forward inboard)
3. CADC Corrections switch ... RESET CORR for a few seconds, then back to NORM (left console middle inboard)
4. Altimeter ... Turn and hold RESET lever for 3 seconds to clear red STBY flag, then set QNH or QFE (instrument panel middle)
  - Do this only after the CADC Corrections switch??
1. Standby Attitude Indicator ... Uncage and center (instrument panel lower right)
2. ADI Flight Director switch ... Horizontal (On) (flat knob on Navigation Mode Selector knob, instrument panel bottom, under Standby ADI)
3. YAW, ROLL, and PITCH STAB. AUG switches ... ENGAGE (left console rear inboard)
4. Trim ... 1 to 3 units nose down (3 recommended) (trim guage is on left forward angled panel outboard)
5. Anti-skid ... ON (left console forward outboard)
6. Exterior lights ... As desired (right console extreme far back)
  - Middle switch position is OFF.