1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Pilot - Guns, Rockets

Fence In
MASTER ARM ... ON

Gun strafing
1. Setup:
  1. Pinky Switch ... GUN (Pinky Hat up, GUN will show on A/A weapon indicator lights)
  2. Sight Mode knob ... CAGE, or A/G if using reticle depression
  3. Reticle Depression knob ... as needed (see below)
  4. Station Select buttons ... GUN (for gun pods, select gun pod stations)
  5. Fuze switch ... ignored
  6. Delivery Mode knob ... OFF or DIRECT
  7. Weapon Selector knob ... not TV or ARM (any other setting OK??)
  8. AWRU INTRVL and QTY knobs ... ignored
  9. RATE switch ... HIGH or LOW as needed (center console left)
2. Press Trigger to fire.
3. NOTE The gun will continue to fire 5 to 11 more rounds (approx 1 sec) after the trigger is released, to clear the gun. This is not affected by the AUTO CLEAR switch (that's only for the external gun pods).

Gun sight depressions (from Heatblur F-4E manual)
Altitude	Speed	Dive Angle	Sight Depression
3000 ft	425 - 450 KCAS	10 - 15°	100 - 110 mil
2500 ft	425 - 450 KCAS	10 - 15°	80 - 90 mil
2000 ft	425 - 450 KCAS	10 - 15°	70 mil
1500 ft	425 - 450 KCAS	10 - 15°	50 - 55 mil
1000 ft	425 - 450 KCAS	10 - 15°	40 - 45 mil

Slower and/or higher altitude will hit low, faster and/or lower altitude will hit high.

Rockets
1. Setup:
  1. Sight Mode knob ... A/G, or CAGE for point-blank
  2. Reticle Depression ... as needed (see below)
  3. Station Selection buttons ... weapon stations selected
  4. Fuze switch ... ignored
  5. Delivery Mode knob ... DIRECT
  6. Weapon Selector knob ... RKTS & DISP
  7. AWRU INTRVL knob and switch ... as needed
  8. AWRU QTY knob ... as needed:
    - C ... (Continuous ripple) While pickle is held, fires one rocket at a time from the outermost selected stations only, at selected intervals. If only one symmetrical station is selected, fires single rockets from that station.
    - S ... (continuous Salvo) While pickle is held, fires one rocket simultaneously from each selected station, at selected intervals. Cycles through pods on MER if equipped.
    - P ... (Pairs) With each pickle press, fires a pair of rockets from the outermost selected symmetrical stations only. Cycles through pods on MER if equipped. If only one symmetrical station is selected, fires pairs from that station. Fires singles from centerline station. Ignores interval.
    - Numbers 1-18 ... While pickle is held, fires up to N rockets total, one at a time from selected stations, outside in, at selected intervals.
1. Put pipper on target, press Red Button to fire.
2. Accuracy is poor.

Rocket sight depressions (from Heatblur F-4E manual)
Altitude	Speed	Dive Angle	Sight Depression
2500 ft	450 - 500 KCAS	10°	30 mil
2500 ft	425 - 475 KCAS	20°	25 mil
3000 ft	400 - 425 KCAS	30°	15 mil
3000 ft	400 - 425 KCAS	45°	0 - 10 mil

Slower and/or higher altitude will hit low, faster and/or lower altitude will hit high.