1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Pilot - CBU Dispensers

Fence In
MASTER ARM ... ON

CBU Dispensers
CBU-2B/A dispensers with BLU-3B bomblets recommended. Other bomblet types have not been tested.
1. Setup:
  1. Sight Mode knob ... CAGE, or A/G
  2. Reticle Depression knob ... as needed, about 120 mils seems right for ~200 ft, ~450 kts delivery, or just aim halfway between the CAGE reticle and bottom of gunsight glass
  3. Station Selection buttons ... weapon stations selected
  4. Fuze switch ... ignored
  5. Delivery Mode knob ... DIRECT
  6. Weapon Select knob ... ROCKETS & DISP
  7. AWRU INTRVL knob and switch ... as needed, 0.01 to 0.05 recommended
    - 0.01 covers about 0.25 nmi, 0.05 covers about 0.5 nmi.
  1. AWRU QTY knob ... S to fire from all dispensers simultaneously, including centerline
    - All other modes fire only from the outermost stations, even if centerline station is also selected.
Press and hold Red Button to drop. Dispensers will fire as long as button is held.
With low altitude attack (~200 ft, ~450 kts), start dropping when target is halfway between the reticle and bottom of gunsight glass.