1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - Pilot - Unguided Bombs, Manual

Fence In
MASTER ARM ... ON

Manual bombing
1. Set up:
  1. Sight Mode knob ... A/G
  2. Reticle Depression knob ... As needed
  3. Station Select buttons ... As needed for desired bombs
  4. Fuze switch ... NOSE & TAIL or as needed (see below for notes)
  5. Delivery Mode knob ... DIRECT
  6. Weapon Selector knob ... BOMBS
  7. AWRU INTRVL knob and switch ... as needed
  8. AWRU QTY knob ... as needed:
    - C ... (Continuous ripple) While pickle is held, drops one bomb at a time from selected stations, outside in, at selected intervals.
    - S ... (continuous Salvo) While pickle is held, drops one bomb simultaneously from each selected station, at selected intervals.
    - P ... (Pairs) With each pickle press, drops a pair of bombs from selected symmetrical stations, outside in. Drops singles from centerline station. Ignores interval.
    - Numbers 1-18 ... While pickle is held, drops up to N bombs total, one at a time from selected stations, outside in, at selected intervals.
1. Manual bombing attacks are left as an exercise to the reader.
2. Press and hold Red Button to drop.
3. Release Red Button when bombs are gone.

Weapon notes
- Retarded bombs (Mk 82 Snakeye and AIR, Mk 84 AIR):
  - NOSE fuze drops slick (non-retarded), NOSE & TAIL drops retarded. TAIL only will result in retarded dud.
- Mk 20 Rockeyes:
  - Use NOSE fuze for PRI timing, NOSE & TAIL for OPT timing. TAIL only will result in dud.

Bomb interval spacing table and notes -- WIP need more data points
- Intervals	0.06 sec	0.10 sec	0.14 sec
  600 kts	60.8 ft	101.3 ft	141.8 ft
  550 kts	55.7 ft	92.8 ft	130.0 ft
  500 kts	50.6 ft	84.4 ft	118.1 ft
  450 kts	45.6 ft	76.0 ft	106.3 ft
  400 kts	40.5 ft	67.5 ft	94.5 ft
  350 kts	35.4 ft	59.0 ft	82.7 ft
- Calculation: kts / 60 / 60 * 6076.115 / interval = distance in ft