1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - Pilot - Unguided Bombs, Timed Loft

Fence In
MASTER ARM ... ON

Loft -- Pre-set target location and Initial Point, timed pullup, automatic bomb release -- WIP needs verification
1. Set up:
  1. (WSO) Set timers.
  2. Delivery Mode knob ... LOFT
  3. Weapon Select knob ... BOMBS
  4. AWRU ... QTY and INT as needed
  5. NOSE/TAIL ARM switch ... As needed
  6. Station Select buttons ... Bomb stations selected
2. When over IP, press and hold Red Button.
3. At pullup point, initiate 4 G pullup.
4. Bombs will release at computed time.
5. Release Red Button when bombs are gone.

Weapon notes
- Retarded bombs (Mk 82 Snakeye and AIR, Mk 84 AIR):
  - NOSE fuze drops slick (non-retarded), NOSE & TAIL drops retarded. TAIL only will result in retarded dud.
- Mk 20 Rockeyes:
  - Use NOSE fuze for PRI timing, NOSE & TAIL for OPT timing. TAIL only will result in dud.

Bomb interval spacing table and notes -- WIP need more data points
- Intervals	0.06 sec	0.10 sec	0.14 sec
  600 kts	60.8 ft	101.3 ft	141.8 ft
  550 kts	55.7 ft	92.8 ft	130.0 ft
  500 kts	50.6 ft	84.4 ft	118.1 ft
  450 kts	45.6 ft	76.0 ft	106.3 ft
  400 kts	40.5 ft	67.5 ft	94.5 ft
  350 kts	35.4 ft	59.0 ft	82.7 ft
- Calculation: kts / 60 / 60 * 6076.115 / interval = distance in ft