1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

509a - A/G - Pilot - AGM-45 Shrike Direct attack

AGM-45 Shrike behavior
- With Direct Attack seeker, missile will start guiding 3 seconds after launch.
- With Loft Attack seeker, missile will remain ballistic until under 18,000 ft MSL and pressure has increased 1 PSI (1,000 to 3,000 ft) since apogee.
- Seeker LOS cone is 45 degrees (22.5 from centerline in all directions). Max seeker detection range seems to be about 27 nmi/50 km.
- Some seekers will give a tone and/or ADI steering on some radars, and some won't. TODO

Fence In
MASTER ARM ... ON

AGM-45 Shrike -- Direct attack, DIRECT mode with Direct seeker
- This is for a short range attack from low to medium altitude. Missile will fly directly at the target, or can be manually lofted for a bit more range.
- IMPORTANT! Before takeoff, on rearming screen, set RF Guidance Unit on missile to appropriate type for target, and set Attack Profile (seeker mode) to Direct Attack.
- Adjust Shrike volume with AURAL TONE knob (left console far aft).
1. Setup:
  1. Sight Mode knob ... CAGE or A/G with 35 mils depression
  2. Station Select buttons ... weapon stations selected
  3. Fuze switch ... ignored
  4. Delivery Mode knob ... DIRECT
  5. Weapon Select knob ... ARM
  6. ADI Flight Director switch ... Horizontal (On) (flat knob on Navigation Mode Selector knob, instrument panel bottom, under Standby ADI)
    - This enables the needles on the ADI to show steering cues from the seeker.
  1. (TGT/MSL REJ switch position doesn't seem to matter...??)
2. Fly toward emitter, following tone volume and needles on the ADI.
3. You will probably need to dive in on the target, missile loses speed very quickly. You can also manually pull up to add some loft, but I haven't tested the angles and ranges yet.
4. When close, press and hold Red Button to fire.
5. Missile will start guiding 3 seconds after launch, and home on any emitter it sees within its 45 degree seeker LOS cone.

Tested attack profiles using Direct Attack seeker
Target type	Seeker	Distance to target	Launch altitude	Launch speed	Launch angle	Result
SA-2	Mk 49 Mod 1	~7 nmi	~500 ft AGL	~550 kts	~10 deg	hit TR
SA-2	Mk 50	6 nmi	1700 ft AGL	540 kts	10 deg	miss, short
SA-2	Mk 50	3.5 nmi	900 ft AGL	480 kts	10 deg	hit TR