1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

509b - A/G - Pilot - AGM-45 Shrike Loft attack

AGM-45 Shrike behavior
- With Direct Attack seeker, missile will start guiding 3 seconds after launch.
- With Loft Attack seeker, missile will remain ballistic until under 18,000 ft MSL and pressure has increased 1 PSI (1,000 to 3,000 ft) since apogee.
- Seeker LOS cone is 45 degrees (22.5 from centerline in all directions). Max seeker detection range seems to be about 27 nmi/50 km.
- Some seekers will give a tone and/or ADI steering on some radars, and some won't. TODO

Fence In
MASTER ARM ... ON

AGM-45 Shrike -- Loft attack, WRCS mode with LOFT seeker, ideally from 20,000 ft AGL or higher
- This is for a visual attack from medium to high altitude. Range is triangulated by putting your pipper on the target, or using the ADI needles. Target altitude must be estimated and set in Jester kneeboard.
- IMPORTANT! Before takeoff, on rearming screen, set RF Guidance Unit on missile to appropriate type for target, and set Attack Profile (seeker mode) to Loft Attack.
- Adjust Shrike volume with AURAL TONE knob (left console far aft).
1. Setup:
  1. Sight Mode knob ... CAGE or A/G (in AGM-45 mode, sight is automatically caged)
  2. Station Select buttons ... weapon stations selected
    - NOTE All selected missiles will be launched automatically, so only select the ones you want to launch.
  1. Fuze switch ... ignored
  2. Delivery Mode knob ... AGM-45
  3. Weapon Select knob ... ARM
    - This activates the missile seeker, and provides steering information to detected emitter.
  1. TGT/MSL REJ switch ... DF REJ (down) (center console)
    - DF REJ uses pitch elevation data from INS, which is more accurate than the missile seeker data. NORM (middle switch position) uses missile seeker data. As of 2024-12-10, both work the same.
  1. WSO (If you are pilot, you'll have to go to the WSO seat and set these up yourself):
    1. WRCS Target Altitude knob ... set to target altitude (use F10 map) (left console middle)
    2. WRCS BIT Mode knob ... AGM-45 (left console middle)
2. ADI needles show steering information (only with some seeker/emitter combos). Fly to center the needles.
  - Bank angle may change steering direction, so multiple corrections may be needed to get the needles centered when wings are leveled.
1. BDHI distance readout will show ground distance to where the pipper is, max range shown is 30 nmi.
2. Put pipper on target (exactly on target if possible), or exactly center the ADI needles.
3. As you put the nose down, the WRCS will continuously calculate whether you're in the Shrike launch envelope based on the distance to the pipper location.
4. As you get within the launch envelope, AOA indicator shows release maneuver that will be required:
  ⋁ -- Close range, launch must be in dive directly at target.
  O -- Medium range, launch in level flight.
  ⋀ -- Long range, launch must be in pullup loft maneuver.
  (no lights = not in range, either too far or too close)
5. You may have to dip the nose to the target several times to check if you're in range.
6. When one of the lights is lit, put the pipper exactly on the target and press and hold Red Button to lock in the range and begin the launch maneuver. (Keep pickle held through the maneuver until missiles launch.)
7. With pickle held, the AOA indicator shows the required maneuver:
  ⋁ -- Push nose down.
  O -- Maintain current attitude for imminent launch (5 seconds or less).
  ⋀ -- Pull nose up and keep pulling until the O is lit.
8. When the O is lit, hold steady until the missiles launch. If you pull up too much, or if you're firing several missiles, you may need to push the nose back down a bit (AOA ⋁ light will illuminate if so).
9. Missiles will automatically launch when in range if Red Button is still held. IMPORTANT All selected missiles will launch one after the other, even if you let go of pickle after first one launches.

OLD (delete this if above steps work after verifying):
AGM-45 Shrike -- WRCS mode, high altitude attack (15k+ ft??)
- IMPORTANT FIXME This mode is currently (2024-05-25) not working as it should. Steps below are what seem to currently work in game.
- IMPORTANT! Before takeoff, set seeker on missile to appropriate type for target. Also set the attack profile to Direct or Loft.
- Adjust Shrike volume with AURAL TONE knob (left console far aft).
1. Setup:
  1. Sight Mode knob ... CAGE or A/G
  2. Station Select buttons ... weapon stations selected
    - NOTE All selected missiles will be launched automatically, so only select the ones you want to launch.
  1. Fuze switch ... ignored
  2. Delivery Mode knob ... AGM-45
  3. Weapon Select knob ... ARM
    - This activates the missile seeker, and provides steering information to detected emitter.
  1. TGT/MSL REJ switch ... DF REJ (down)
    - DF REJ uses pitch elevation data from INS, which is more accurate than the missile seeker data. NORM (middle switch position) uses missile seeker data.
  1. WSO (If you are pilot, you'll have to go to the WSO seat and set these up yourself):
    1. WRCS Target Altitude knob ... set to target altitude (use F10 map) (left console middle)
    2. WRCS BIT Mode knob ... AGM-45 (left console middle)
2. ADI needles show steering information. Fly to center the needles.
  - Bank angle may change steering information, so multiple corrections may be needed to get the needles centered when wings are leveled.
1. Put pipper on target (exactly on target if possible).
2. Press and hold Red Button.
3. BDHI readout distance readout should show ground distance to target (ground under pipper).
4. When you get closer, AOA indicator shows release maneuver:
  ⋁ -- Dive
  O -- Level, or maintain current attitude for imminent launch
  ⋀ -- Pullup
5. Maneuver in accordance with AOA lights instruction.
6. Missile will automatically launch when in range if Red Button is still held. IMPORTANT All selected missiles will launch one after the other, even if you let go of pickle after first one launches.