1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Cold Start

Cold Start
Ignition key ... On (rotated, not fore/aft) (center console under collective handle)
  - Leave this off to get an easter egg when you try the START switch...
1. BATT 1 switch ... On (forward) (overhead forward panel)
2. IGN and FADEC switches ... On (forward) (overhead forward panel)
3. Throttle ... Idle position (collective grip) (mapped to Home key)
4. Audio warning tone ... cancel with ACK switch (down) (center console top center)
5. START switch ... ON and hold for a few seconds until engine begins spooling up (collective head)
  - Engine should continue spooling up to idle at ~64.1% RPM.
  - Audio warning tone ... cancel with ACK switch (down) (center console top center)
1. When engine is at idle, proceed.
2. DC GEN, AC GEN, and RUN ESNTL BUS switches ... On (forward) (overhead forward panel)
3. FUEL BOOST switch ... On (forward) (overhead forward panel)
4. All circuit breakers and switches on rear vertical CB panel On or Pushed In:
  1. PART SEP CB (engine particle separator) (bottom right)
  2. RADAR DETR and WARN switches (top left)
  3. IFF switch (top right)
  4. HF switch (top left)
5. CMWS CB switch ... On (forward) (CB box above, left, and just behind pilot's head)
6. Throttle ... slowly to Max (throttle increase/decrease mapped to Numpad+/Numpad-)
7. MPD (Multiparameter Display) ... Select switch +/- to NR (digital "chicklet" display, instrument panel center bottom, just above center console)
8. Incr/Decr ("Inker-Dinker") switch ... +/- as needed (right-click 2x) to set NR to 100 (collective head)
  - When at 100, NR "chicklet" light should be just one light resting on the 100 line.
1. MMS Mode knob ... PREPT or FWD (instrument panel lower left, above CPG left knee)
2. SCAS PWR switch, then PITCH/ROLL and YAW switches ... On (center console right)
3. Alignment is shown in INITIAL PAGE > NAV ALIGN on MFD. Should start aligning automatically when BATT 1 is turned on, takes about 2.5 mins.
  - When done, GC ALIGN at bottom of MFD screen goes away and "AUTO" on AUTO/MANUAL OSB gets unboxed.
  - To return to the Pilot INITIAL PAGE, press round INIT button below the MFD frame, not the square INIT button at the bottom center of the frame itself.
  - To return to the Copilot INITIAL PAGE, momentary IDM/INIT switch to INIT (below CPG MFD).
1. CMWS PWR knob ... momentarily to TEST, then ON (CMWS control box, instrument panel top center)
2. CMWS dispenser AUTO/BYPASS switch ... BYPASS recommended (center console lower panel rear, below collective handle)
3. Lights ... As needed:
  - Overhead forward panel:
    - Console lights
    - Instrument panel lights
    - Cockpit flood lights and brightness
    - Position lights
    - Anti-collision lights
  - Above, left, and just behind pilot's head:
    - Formation lights
    - IR beacon
1. Master Arm switch ... ARMED (center console upper panel bottom)
2. Laser Arm switch ... ARM (instrument panel far left)
3. LMC switch ... ON (stabilizes the MMS) (under copilot MFD)