1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Cold Start

Cold Start -- WIP
1. Canopy ... Close
2. MSTR IGN knob ... BATT (or EXT PWR if using external power; set to BATT after APU is started)
  - Must start APU within 1 minute if temp > 43 deg C/109 deg F, 3 mins if temp between 32-43 deg C, 20 mins if temp < 32 deg C.
Lights ... As needed (left console rear)
  - IMPORTANT: INTR LT PRIMARY knob (left console rear) must be turned up to see boresight reticle.
APU start button ... Press to start APU (guarded button, left console just behind MSTR IGN knob)
  - DOPPLER nav system starts aligning automatically. You can check status on TSD > UTIL page, POSITION CONFIDENCE section shows alignment progress: white numbers turn green when finished (takes 3m55s from when APU begins providing power). The Dash 10 manual says: "There is no effect on the NAV system accuracy if the engines are started, or if the main rotor is turning during alignment." (p. 374, 3-68)
  - APU start takes 30 seconds, MFDs come on at the end.
Radio SQL switches ... Forward (they spring back to neutral) to enable squelch on all 5 radios (sets squelch for both PLT and CPG) (right console forward)
  - Squelched radios show a '*' next to the radio in the UFC.
1. Set clock to ZULU or LOCAL time ... TSD OSB > UTIL OSB (T6) > TIME OSB (R2)
2. Reset WCA (Warning/Caution/Advisory): [M] OSB > DMS OSB ([M]) > WCA OSB > RESET OSB.
3. SAI ... Uncage (hold right-click while scrolling) (right instrument panel)
4. Go to ENG page on either MFD ([M] OSB -> ENG OSB) before starting engines
5. Start first engine (either engine can be started first):
  - Cold engine (4 hours since last shutdown):
    1. ENG START switch ... START (right click) (left console outboard)
    2. When NG% starts going up, POWER lever ... IDLE (RAlt-Home for engine 1, RShift-Home for engine 2)
  - Warm engine
1. ENG START switch ... IGN OVRD (left click and hold)
2. Allow NG% to increase to 18-20%, then ENG START switch ... OFF (release left click)
3. When NG% is back below 5%, ENG START switch ... START (right click)
4. POWER lever ... IDLE
1. Start second engine:
  1. Follow steps above for conventional startup.
  - For cross-engine start:
    1. Go to ENG page ([M] OSB -> ENG OSB)
    2. Increase collective to 95% NG on the other engine.
    3. Follow steps above for cold or warm engine start.
    4. Collective ... reduce to flat pitch
2. Wait for oil pressure for both engines to be less than 70 PSI (ENG page).
3. POWER levers ... Advance smoothly to FLY (Numpad + and hold to advance both, use short increments)
  - NR% and NP% should stabilize at 101%.
APU ... OFF (press APU button) and close cover
  - APU ON text should disappear from UFC.
Boresight HMD: [WPN] OSB > BORESIGHT OSB > IHADSS OSB > line up HMD LOS crosshair in boresight rings > B/S NOW OSB (you can also click B/S NOW with Cursor Enter (Ministick press)
  - IMPORTANT: INTR LT PRIMARY knob (left console rear) must be turned up to see boresight reticle.
1. RLWR system ... On: [M] OSB > ASE OSB > UTIL OSB > RLWR OSB (circle is solid when enabled)
2. RLWR volume ... As needed (right console forward, volume knob on radios panel, AUX section)
3. Chaff system ... ARM: [M] OSB > ASE OSB > UTIL OSB > CHAFF OSB
  - Master Arm or GND ORIDE must be ON to arm the chaff system.
1. (If CPG) CPG laser on ... WPN > UTIL > LASER
2. If FCR is equipped, power on FCR:
  1. FCR page
  2. UTIL OSB
  3. MMA OSB to go from PINNED to NORM
  4. FCR BIT ORIDE OSB to cancel FCR BIT tests and make the radar active

Proceed with remaining takeoff checklist on next page.