1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start
1. BATT switch ... ON (roof panel forward left)
2. APU switch ... RDY for 5 seconds, then START for 2 seconds, then release back to RDY (roof panel forward left)
3. When APU RDY light illuminates and UTIL PRES light goes out (roof panel forward left), proceed.
4. GEN, APU switch ... ON (roof panel forward left)
5. MFD power knobs ... NORM or NVG as needed (pilot left/right, copilot left/right, and center)
6. Bring up INST display on one of the MFDs to monitor engine start.
7. Crossfeed switch ... ON (roof panel aft middle)
8. B/U PWR switch ... ON (roof panel forward middle)
9. ?? PWR XFER 1 and PWR XFER 2 switches ... ON (roof panel forward right)
10. Start engine 1:
  1. Engine 1 FUEL CONTR, MAIN, AFT and FWD switches ... ON (roof panel aft middle)
  2. Engine 1 control lever (white handle) ... Move slowly from STOP to GROUND (roof panel middle)
  3. ENG START switch ... 1 and hold (left click and hold) (roof panel forward middle)
  4. When Engine 1 NG is 12% or more, release.
  5. When Engine 1 NG is at 55%, proceed.
11. Start engine 2:
  1. Engine 2 FUEL CONTR, MAIN, AFT and FWD switches ... ON (roof panel aft middle)
  2. Engine 2 control lever (white handle) ... Move slowly from STOP to GROUND (roof panel middle)
  3. ENG START switch ... 2 and hold (right click and hold) (roof panel forward middle)
  4. When Engine 2 NG is 12% or more, release.
  5. When Engine 2 NG is at 55%, proceed.
12. Engine 1 and Engine 2 control levers ... Move slowly from GROUND to FLIGHT
13. When NR is at 100%, proceed
14. GEN 1 and 2 switches ... ON (roof panel forward left)
15. GEN APU switch ... OFF (roof panel forward left)
16. APU switch ... OFF (roof panel forward left)