1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - AOA, Air Refueling

AOA rules of thumb
- 8-10 units for best acceleration
- 14/14.5 units for max range cruise (up to/above 25,000 ft)
- 18/17 units for max endurance (up to/above 25,000 ft)
- 16-22 units for optimum, energy-sustaining turns
- 20-22 units for landing on-speed
- 28-30 units for best turn rate (full aft stick to either G limit or 30 units AOA)
- 30 units max AOA

Air Refueling
1. Pilot Director Lights on the bottom of the tanker tell your position. The lights within the bars show your position relative to the tanker and the refueling position. Fly opposite the direction of the lights to correct your position.
2. Left light is your vertical position. If light is forward of center, you are too low and you need to go up. If light is aft of center, you are too high and you need to go down.
3. Right light is your horizontal position (forward/aft). If light is forward of center, you are too far forward and need to go back. If light is aft of center, you are too far aft and need to go forward.
4. Open A/R refueling slipway (switch on left console outboard, just forward of throttle).
5. Position center of your plane about under the right wing/fuselage connection of the tanker to put your refueling door on the tanker's centerline.