1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

404 - A2A - IFF, AAI, EID, NCTR

IFF and AAI/EID/NCTR general info
- "IFF" refers to what you are transmitting to identify yourself. "Interrogate/Interrogation" is what you do to a contact to determine if it's friendly (AAI and EID).
- AAI is Air-to-Air Interrogation, EID is Enhanced Identification (which includes NCTR).
- In DCS, you normally only have to use Mode 4A (and maybe rarely Mode 4B, or Mode 3).

IFF setup, squawk codes
- UFC main menu shows current active modes next to L3 OSB.
- Press L3 OSB to go to "-IFF-" page:
  - Phases
    - Phases 1-13 can be programmed with the PROGRAM OSB (R3 OSB) to have their own codes and turn on at the given time. Current phase is shown next to L1 OSB and active time?? next to R1 OSB.
    - Notso says this works, but it's not really useful unless the mission is set up to require doing it.
    - I assume Phase 0 is "phases off".
  - Toggle Modes 1, 2, and 3 on/off with L2, L3, and L4 OSBs when scratchpad is empty.
  - Mode 1:
    - Enter new code in NN format (N=0-7) on scratchpad, press L2 OSB.
  - Mode 2:
    - Code can only be changed in Mission Editor.
  - Mode 3:
    - Enter new code in NNNN format (N=0-7) on scratchpad, press L2 OSB.
    - Toggle Mode C (adds pressure altitude to M3 transmission) with R2 OSB.
    - Mode 3 is the regular civilian transponders, common codes:
      - 1200 - Civil VFR flights
      - 4000 - Military VFR flights
      - 7000 - VFR when no other code assigned
      - 7700 - Emergency
    - To "ident" in Mode 3, press and hold I/P button on UFC.
  - Mode 4:
    - Controlled with IFF MODE switch on left console rear outboard:
      - OUT is off, A or B is on (A is the current day's code, B is the code for the following day, usually should leave in A)
  - AAI SLV OSB ... If enabled, I think this sets the AAI system to interrogate with the same modes you have enabled here. If you then disable AAI SLV, the AAI modes remain enabled until you turn them off manually in the AAI menu (see below).

AAI/EID setup
- UFC main menu shows current active modes next to R3 OSB.
- Press L3 OSB to go to "-AAI-" page:
  - Press R3 OSB to toggle between AAI and EID pages.
  - Mode 1, 2, and 3:
    - The letter following the code is C for Correct, or N for Normal. If C, contact will only show friendly if they respond in that mode with the correct code. If N, contact will show friendly if they respond in that mode with any code.
  - Mode 4:
    - Enter A, B, or AB in scratchpad and press L4 OSB to set whether to interrogate the A code, B code, or A and B.
  - BARS:
    - 2 or 4, determines the number of radar bars (horizontal sweeps) the interrigator will be active during??
  - AUTO ID:
    - STT -- Auto-interrogates STT (Single Target Track) targets.
    - PDT -- Auto-interrogates STT targets, or the PDT (Primary Designated Target) in TWS modes.

Interrogating radar contacts
- With A/A radar page as SOI:
- Interrogate with AAI modes:
  - Coolie switch (Middle Finger Hat) left long to use AAI. Status is shown on the lower right of the radar screen. Each selected AAI mode (4, 1, 2, and 3) will be checked in sequence for the number of AAI bars selected.
- Interrogate with EID modes, including NCTR:
  - Coolie switch (Middle Finger Hat) right long to use EID. Status is shown on the lower right of the radar screen. Each selected EID mode (4, 1, 2, and 3) will be checked in sequence for the number of EID bars selected.
  - Additionally, if target is within NCTR parameters (~25 nmi, +/-30 deg head or tail aspect??), target type will be shown.

Sources
- https://www.youtube.com/watch?v=-UES3P9z9J8
- https://www.youtube.com/watch?v=HgG0TQ6DbmM