1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Unguided bombs

Master Arm ... ON
Master Mode ... A/G

Gun/Strafing
1. Select GUN and STRF on SMS page.
2. If using CCIP/CCRP weapons, pressing Flip-down Trigger will cycle CCIP/CCRP/STRF.
3. Radar should be on (or in standby) for ranging, or TPOD laser can be used (LASER ARM switch ON).
4. Pipper on HUD shows range. 12000 ft at the top, 6000 ft (in range) at the bottom.
5. Press Trigger to fire.

Rockets
1. Select rockets (nnM151, where nn is number of rockets remaining) on SMS page.
2. Radar should be on (or in standby) for ranging, or TPOD laser can be used (LASER ARM switch ON).
3. Pipper on HUD will have a short horizontal bar above it when in range, 8000 ft slant.
4. Press Red Button to fire.

CCIP/CCRP bombing
1. Select bombs in SMS page.
2. Set SGL/PAIR, interval, and RPL settings with OSBs.
3. Press Flip-down Trigger to cycle CCIP/CCRP/STRF modes, or press the OSB at the top of the SMS page.
4. Press Red Button to drop.
- If CCIP fall line has small horizontal bar on it ("reflected cue"), put CCIP dot on target and hold pickle to enter CCRP mode until bombs drop.
- With CBU 87 and CBU 97, NSTL fuze makes it burst at height shown on SMS page, NOSE fuze makes it burst immediately.
Toss bombing with CCRP
1. Set desired release angle on SMS > CNTL > REL ANG (bottom right). Default is 45 deg. 25-30 deg recommended.
2. At about 10 nmi from the target, range diagram will appear on right side of HUD. Caret shows your current range to the target, "staple" shows the toss envelope. Timer at bottom right of HUD shows time to reach max toss range (top of staple).
3. At 10?? seconds from max toss range (top of staple), two cues appear on azimuth steering line:
  - Short thick bar coming down from the top is the range cue. When it reaches the velocity vector, you will begin the pull-up.
  - Long thin bar coming up from the bottom is the pull-up cue; when you begin the pull-up, you'll pull to keep the velocity vector on that line as it continues up to the release angle.
1. At 2 seconds from max toss range (top of staple), the Max Toss Anticipation Cue appears: a large circle on the HUD. It's just to alert you to be ready to do the pullup.
2. Press and hold pickle button.
3. At the max toss range, the two cues intersect at the velocity vector, the large circle begins flashing for 2 seconds, the short thick bar resets to the top of the azimuth steering line, and the wide thin bar zooms upwards. Pull to follow the wide thin bar, approx 4 G.
4. Bombs will release automatically when the velocity vector meets the range cue (short thick bar).