1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504b - A/G - ATGMs as human gunner

9K144 Shturm (AT-6 Spiral) -- Max range ~5.5 km/2.7 nmi/3.1 mi
9M120 Ataka (AT-9 Spiral-2) -- Max range ~6.0 km/3.2 nmi/3.7 mi)
- 9M120 -- Tandem HEAT warhead
- 9M120F -- HE warhead
- 9M120O -- A/A expanding rod warhead and proximity fuze (4 meters)

Manual attack with ATGMs as human gunner
Setup
1. CPG: SAFETY SWITCHES ... ON (gang-bar switch on left wall)
2. CPG: MISSILE POWER switch ... ON (right instrument panel)
3. CPG: Launcher PWR switch ... ON (black box with station select knob, right console front)
  - Missiles take 3-4 mins to warm up. READY light on Launcher control box will illuminate when ready.
CPG: GUID. UNIT POWER switch ... ON (sight control box, right console rear)
  - Sight takes 3 minutes to warm up. READNS light on panel below sight control box will illuminate.
1. CPG and PLT: Select Weapon knob ... OFF/MSL (slaves pilot's floating reticle to ATGM scope LOS)
2. CPG: Weapon Selection Control Handover switch ... ?? (green guarded switch, left instrument panel) -- Not sure what this switch does, or if it's needed...
Controls
- Sight controls are on Dish Hat:
  - OBSERV switch toggle ... Dish Hat press
  - DIAFR switch toggle ... Shift-Dish Hat press (when OPEN/up, overrides ATGM shoot limits)
  - Lean into sight toggle ... Dish Hat up
  - Zoom toggle ... Dish Hat down
  - Sight reticle illumination and filters:
    - Reticle illumination (backlight) ... Shift-Dish Hat up
    - Orange contrast filter ... Shift-Dish Hat right
    - Green laser filter ... Shift-Dish Hat left
- Launcher controls are on Gray Reset Hat:
  - Reset emitter ... Gray Reset Hat back
  - Prev/Next missile station ... Gray Reset Hat left/right
Engagement flow
Missile station select knob ... As needed to select pylon (Gray Reset Hat left/right)
  - From pilot/gunner's perspective, ATGM tubes are numbered left to right: 1, 2, 5, 6, 7, 8, 3, 4
  - MSL ON LNCHR light will illuminate if selected tube is loaded.
1. Pilot lines up on target.
2. OBSERV switch ... ON (Dish Hat press) (turns on sight stabilization gyros and opens sight doors)
  - L3 light will start blinking, L4 light will go in in 10-15 seconds, sight is now ready and can be moved.
  - IMPORTANT: Maneuvering limits are +/-25 deg pitch and bank with OBSERV ON.
  - If gyro gets tumbled: Turn GUID. UNIT POWER switch OFF, wait 3 minutes, then turn it back ON.
1. Look through sight (Dish Hat up) and acquire target. Dish Hat down to toggle zoom (3x/10x).
2. Use ranging reticle on left side of sight to estimate range. When a tank or APC is about the height of the "50" mark, it should be about 5 km away??
3. Pilot maneuvers helicopter to put floating reticle inside the inner ring of the fixed reticle.
  - Red light in ATGM sight and continuous tone will sound indicating within launch parameters.
1. Fire missile with Red Button. Launches after 0.9 sec delay.
2. Keep sight on target until missile hits.
3. After missile hits: Gray Reset Hat back to reset transmitter. Gray Reset Hat right to select next missile.
4. When finished, OBSERV switch ... OFF (Dish Hat press) and leave sight (Dish Hat up).

With Petrovich AI as pilot
Trim Hat left short to cycle through AI flight modes (FLT -> CBTM -> HVR -> HVRT).
1. Use FLT mode to set speed, heading, and altitude (Trim Hat right short once to show turn-to marker; Trim Hat right short again to tell pilot to turn where you're looking).
2. Go to CBTM mode when approximately on heading.
3. Go to sight, get on target, press Trim Hat up short to tell pilot to align to sight LOS.
4. When ready to shoot, press Trim Hat up long to tell the pilot to dip the nose and align the sights for firing.
5. Fire when you have red light and tone.
6. When done, OBSERV OFF and press Trim Hat down long to tell pilot to do a 180 deg evasive turn away from the target.
Voice calls
- "Observe on" ... When OBSERV switch is turned ON and pilot should restrict maneuvering.
- "Searching" ... When leaning into sight.
- "In range" ... When target is in range.
- "Firing" or "Rifle" ... When firing missile.
- "Observe off" ... When OBSERV switch is turned OFF and pilot is free to maneuver.